## Slide 1: Intel 8085

## Slide 2
Fig: Functional Block Diagram of 8085A microprocessor

## Slide 3: Internal Architecture of 8 bit microprocessor and its registers:
The Intel 8085A is a 8 bit general purpose microprocessor capable of addressing 64K of memory.
The main components of 8085A are array of registers, the arithmetic logic unit, the encoder/decoder, and timing and control circuits linked by an internal data bus.
ALU
The arithmetic logic unit performs the computing functions.
It includes the accumulator, the temporary register, the arithmetic and logic circuits and five flags.
The temporary register is used to hold data during an arithmetic/logic operation.
The result is stored in the accumulator.
The flags (flip-flops) are set or reset according to the result of the operation.

## Slide 4
2. Accumulator (register A):
This register is used to store the 8-bit data and to perform arithmetic and logic operations and 8085 microprocessor is called accumulator based microprocessor.
When data is read from input port, it first moved to accumulator and when data is sent to output port, it must be first placed in accumulator.
3. Temporary registers(W & Z):
They are 8 bit registers not accessible to the programmer.
During program execution, 8085A places the data into it for a brief period.
4. Instruction register(IR):
It is a 8 bit register not accessible to the programmer.
It receives the operation codes of instruction from internal data bus and passes to the instruction decoder which decodes so that microprocessor knows which type of operation is to be performed.

## Slide 5
5. Register Array:
(Scratch pad registers B, C, D, E):
It is a 8 bit register accessible to the programmers.
Data can be stored upon it during program execution.
These can be used individually as 8-bit registers or in pair BC, DE as 16 bit registers.
The data can be directly added or transferred from one to another.
Their contents may be incremented or decremented and combined logically with the content of the accumulator.
Register H & L: - They are 8 bit registers that can be used in same manner as scratch pad registers.

## Slide 6
Stack Pointer (SP): -
stack is an area of memory set aside for the purpose of storing data.
The location of the memory is defined by the 16 bit register called SP.
When a data is stored its value is decreased by 1 while it is increased by 1 when the data is retrieved.
Program Counter (PC): -
Microprocessor uses the PC register to sequence the execution of the instructions.
The function of PC is to point to the memory address from which the next byte is to be fetched
When a byte is being fetched, the PC is incremented by one to point to the next memory location.

## Slide 7
6. Flags:
Register consists of five flip flops, each holding the status of different states separately is known as flag register and each flip flop are called flags.
8085A can set or reset one or more of the flags and are sign(S), Zero (Z), Auxiliary Carry (AC) and Parity (P) and Carry (CY).
The state of flags indicates the result of arithmetic and logical operations, which in turn can be used for decision making processes.
The different flags are described as:

## Slide 8
Carry: - If the last operation generates a carry its status will 1 otherwise 0. It can handle the carry or borrow from one word to another.
Zero: - If the result of last operation is zero, its status will be 1 otherwise 0. It is often used in loop control and in searching for particular data value.
Sign: - If the most significant bit (MSB) of the result of the last operation is 1 (negative), then its status will be 1 otherwise 0.
Parity: - If the result of the last operation has even number of 1’s (even parity), its status will be 1 otherwise 0.
Auxiliary carry: - If the last operation generates a carry from the lower half word (lower nibble), its status will be 1 otherwise 0. Used for performing BCD arithmetic.

## Slide 9
7. Timing and Control Unit:
This unit synchronizes all the microprocessor operations with the clock and generates the control signals necessary for communication between the microprocessor and peripherals.
The control signals are similar to the sync pulse in an oscilloscope.
The RD and WR signals are sync pulses indicating the availability of data on the data bus.
8. Interrupt controls: The various interrupt controls signals (INTR, RST 5.5, RST 6.5, RST 7.5 and TRAP) are used to interrupt a microprocessor.
9. Serial I/O controls: Two serial I/O control signals (SID and SOD) are used to implement the serial data transmission.

## Slide 10
Fig: Pin Diagram of 8085
SID (Serial Input Data)
SOD (Serial Output Data).

## Slide 11: Characteristics (features) of 8085A microprocessor & its signals
The 8085A (commonly known as 8085) is a 8-bit general purpose microprocessor capable of addressing 64K of memory.
The device has 40 pins, require a +5V single power supply and can operate with a single phase clock.
1. Address bus:
  The 8085 has 16 signal lines that are used as the address bus; however, these lines are split into two segments A15-A8 and AD7- AD0.
  The eight signals A15-A8 are unidirectional and used as high order bus.
2. Data bus:
  The signal lines AD7- AD0 are bidirectional, they serve a dual purpose. They are used the low order address bus as well as data bus.
3. Control and status signals:
  This group of signals includes two control signals (RD and WR), three status signals (IO/M ,S1 and S0) to identify the nature of the operation, and one special signals (ALE) to indicate the beginning of the operation.

## Slide 12
ALE- Address Latch Enable: This is a positive going pulse generated every time the 8085 begins an operation (machine cycle): it indicates that the bits AD7-AD0 are address bits, when pulse goes high. Otherwise indicates data.
Read: this is a read control signal(active low). This signal indicates that the selected I/O or memory device is to be read and data are available on the data bus.
Write: This is a write control signal (active low) . This signal indicates that the data on the data bus are to be written into a selected memory or I/O location.
IO/M: This is a status signal used to differentiate between I/O and memory operations. When it is high , it indicates an I/O operation; When it is low indicates a memory operation. This signal is combined with (Read) and (Write) to generate I/O and memory signals.
S1 and S0 : These status signals, similar to IO/M, can identify various operations, but they are rarely used in small systems.

## Slide 13
4. Power Supply and Clock frequency:
VCC: +5V power supply
VSS: Ground reference
X1 and X2: A crystal (RC or LC network) is connected at these two pins for frequency.
CLK OUT: It can be used as the system clock for other devices.
Externally Initiated signals: -
INTR (input): interrupt request, used as a general purpose interrupt.
INTA (Output): This is used to acknowledge an Interrupt.
RST 7.5, 6.5, 5.5 (inputs): These are vectored interrupts that transfer the program control to specific memory locations.
  They have higher priorities than INTR interrupt.
  Among these three, the priority order is 7.5, 6.5, and 5.5.
TRAP (input): This is a non-maskable interrupt with highest priority.

## Slide 14
HOLD (input): This signal indicates that a peripheral such as a DMA( Direct Memory Access) controller is requesting use of Address and data bus.
HLDA (output): Hold Acknowledge: This signal acknowledges the HOLD request
READY (Input) : This signal is used to delay the microprocessor Read or Write cycles until a slow- responding peripheral is ready to send or accept data. When this signal goes low, the microprocessor waits for an integral number of clock cycles until it goes high.
RESETIN: When the signal on this pin goes low, the program counter is set to zero, the buses are tri-stated, and MPU is reset.
RESET OUT: This signal indicates that the MPU is being reset. The signal can be used to reset other devices.
Serial I/O ports: The 8085 has two signals to implement the serial transmission: SID (Serial Input Data) and SOD (Serial Output Data). In serial transmission, data bits are sent over a single line, one bit at a time, such as the transmission over telephone lines.

## Slide 15
Introduction to 8085 Instructions

## Slide 16
Instruction and Data Formats
Each instruction has two parts.
The first part is the task or operation to be performed. This part is called the “opcode” (operation code).
The second part is the data to be operated on Called the “operand”.
The operand (or data) can be specified in various ways.
It may include 8-bit (or 16-bit) data, an internal register, a memory location, or an 8-bit (or 16-bit) address.
Example: ADD R1, R0
Here R0 is the source register and R1 is the destination register. The instruction adds the contents of R0 with the content of R1 and stores result in R1.

## Slide 17
Instruction Size
Depending on the number of address specified in instruction sheet, the instruction format can be classified into the categories.
One address format (1 byte instruction): Here 1 byte will be Op-code and operand will be default. E.g. ADD B, MOV A,B
Two address format (2 byte instruction) :Here first byte will be Op-code and second byte will be the operand/data(8-bit data). E.g. MVI A, 8-bit Data
Three address format (3 byte instruction): Here first byte will be Op-code, second and third byte will be operands/data(16-bit data). That is 2nd byte- lower order data. 3rd byte – higher order data. E.g. LXI B, 4050

## Slide 18: Addressing modes:
The various format (way) of specifying the operands are called addressing mode.
So addressing mode specifies where the operands are located rather than their nature.
The 8085 has 5 addressing mode:
  Direct addressing mode
  Register Direct addressing mode
  Register Indirect addressing mode
  Immediate addressing mode
  Implied or Inherent addressing mode

## Slide 19
1. Direct addressing mode:
The instruction using this mode specifies the effective address as part of instruction.
The instruction size either 2-bytes or 3-bytes with first byte op-code followed by 1 or 2 bytes of address of data.
E. g. LDA 9500H
IN 40H
This type of addressing is called absolute addressing.
2. Register Direct addressing mode:
This mode specifies the register or register pair that contains the data.
E g. MOV A, B
Here register B contains data rather than address of the data.

## Slide 20
3. Register Indirect addressing mode:
In this mode the address part of the instruction specifies the memory whose contents are the address of the operand.
So in this type of addressing mode, it is the address of the address rather than address itself. (One operand is register)
e. g. MOV R, M MOV M, R STAX, LDAX etc.
STAX B
4. Immediate addressing mode:
In this mode, the operand position is the immediate data.
For 8-bit data, instruction size is 2 bytes and for 16 bit data, instruction size is 3 bytes.
E.g. MVI A, 32H
LXI B, 4567H

## Slide 21
5. Implied or Inherent addressing mode:
The instructions of this mode do not have operands.
E.g. NOP: No operation
HLT: Halt
EI: Enable interrupt
DI: Disable interrupt

## Slide 22
Classification of an instruction
An instruction is a binary pattern designed inside a microprocessor to perform a specific function (task). The entire group of instructions called the instruction set. The 8085 instruction set can be classified in to 5- different groups.
Data transfer group
Arithmetic group
Logical group
Branching group
Miscellaneous group: The instructions relating to stack operation, controlling purposes such as interrupt operations are fall under miscellaneous group including machine control like HLT, NOP.

## Slide 23
Data transfer group instructions:
This group of instruction copy data from a source location to destination location without modifying the contents of the source.
The transfer of data may be between the registers or between register and memory or between an I/O device and accumulator.
None of these instructions changes the flag.
The instructions of this group are:
1. MOV Rd, Rs (move register instruction)
1 byte instruction
Copies data from source register(Rs) to destination register(Rd).
Rd & Rs may be A, B, C, D, E, H & L
E.g. MOV A, B

## Slide 24
2. MVI R, 8 bit data (move immediate instruction)
2 byte instruction
Loads the second byte ( 8 bit immediate data) into the register specified.
R may be A, B, C, D, E, H & L
E.g. MVI C, 53H
3. MOV M, R (Move to memory from register)
Copy the contents of the specified register to memory. Here memory is the location specified by contents of the HL register pair.
E.g. MOV M, B
4. MOV R, M (move to register from memory)
Copy the contents of memory location specified by HL pair to specified register.
E. g. MOV B, M

## Slide 25
5. LXI RP, 2 bytes data (load register pair)
3-byte instruction
Load immediate data to register pair
Register pair may be BC, DE, HL & SP(Stack pointer)
1st byte- Op-code
2nd byte - lower order data
3rd byte - higher order data
E.g. LXI B, 4532H; B 45, C 32H
6. MVI M, data (load memory immediate)
2 byte instruction.
Loads the 8-bit data to the memory location whose address is specified by the contents of HL pair. E.g. MVI M , 35H; [HL] 35H

## Slide 26
7. LDA 4035H (Load accumulator direct)
3-byte instruction
Loads the accumulator with the contents of memory location whose address is specified by 16 bit address.
A [4035H]
8. LDAX RP (Load accumulator indirect)
1 byte instruction.
Loads the contents of memory location pointed by the contents of register pair to accumulator.
E. g. LDAX B [A] [[BC]]
LXI B, 9000H  B= 90, C= 00
LDAX B A= [9000]

## Slide 27
9. STA 16-bit address (store accumulator contents direct)
3-byte instruction.
Stores the contents of accumulator to specified address
E.g. STA FA00H [FA00][A]
10. STAX RP [RP]  A
Stores the contents of accumulator to memory location specified by the contents of register pair.
1 byte instruction
E.g. STAX B

## Slide 28
11. IN 8-bit port address
2-byte instruction
Read data from the input port address specified in the second byte and loads data into the accumulator i.e. input port content to accumulator:
E. g. IN 40H
12. OUT 8-bit port address
2-byte instruction
Copies the contents of the accumulator to the output port address specified in the 2nd byte. That means accumulator to output port:
E.g. OUT 40H

## Slide 29
13. LHLD 16-bit address ( Load HL directly)
3-byte instruction.
Loads the contents of specified memory location to L –register and contents of next higher location to H-register.
E.g. LHLD 9500H
14. SHLD 16-bit address (store HL directly)
Opposite to LHLD.
Stores the contents of L-register to specified memory location and contents of H-register to next higher memory location.
E.g. SHLD, 9500H

## Slide 30
15. XCHG (Exchange)
Exchanges DE pair with HL pair.
Eg:
LXI H, 7500H H= 75, L=00
LXI D, 9532H D=95. E=32
XCHG H=95, L=32 D=75 E=00

## Slide 31
Arithmetic group Instructions
The 8085 microprocessor performs various arithmetic operations such as addition, subtraction, increment and decrement.
These arithmetic operations have the following mnemonics.
1. ADD R/M
1 byte add instruction.
Adds the contents of register/memory to the contents of the accumulator and stores the result in accumulator.
E.g. Add B A [A] + [B]

## Slide 32
2. ADI 8 bit data
2 byte add immediate instruction.
Adds the 8 bit data with the contents of accumulator and stores result in accumulator.
E.g. ADI 9BH A  A+9BH
3. SUB R/M
1 byte subtract instruction.
Subtracts the contents of specified register/memory with the contents of accumulator and stores the result in accumulator.
E.g. SUB D A [A] - [D]

## Slide 33
4. SUI 8 bit data
2 byte subtract immediate instruction.
Subtracts the 8 bit data from the contents of accumulator stores result in accumulator.
E. g. SUI D3H; A  A - D3H
5. INR R/M, DCR R/M
1 byte increment and decrement instructions.
Increase and decrease the contents of R(register) or M(memory) by 1 respectively.
E.g. DCR B ; B=B-1
DCR M ; [HL] = [HL]-1
INR A ; A=A+1
INR M ; [HL] +1

## Slide 34
6. INX Rp, DCX RP
Increase and decrease the register pair by 1.
Acts as 16 bit counter made from the contents of 2 registers (1 byte instruction)
E.g. INX B ; BC=BC+1
DCX D ; DE=DE-1
ADC R/M and ACI 8-bit data
ADC R/M ( addition with carry (1 byte))
ACI 8-bit data ( immediate addition with carry (2 byte).
Adds the contents of register or 8 bit data whatever used suitably with the Previous carry.
E.g. ADC B ; A  A+B+CY
ACI 70H ; A  A + 70+CY

## Slide 35
8. SBB B/M
1 byte instruction.
Subtracts the contents of register or memory from the contents of accumulator and stores the result in accumulator.
E.g. SBB D ; A =A-D-Borrow
9. SBI 8 bit data
2 byte instruction.
Subtracts the 8-bit immediate data from the content of the accumulator and stores the result in accumulator.
E.g. SBI 70H ; A =A-70-Borrow

## Slide 36
10. DAD Rp(double addition)
1 byte instruction.
Adds register pair with HL pair and store the 16 bit result in HL pair.
E.g.
LXI H, 7320H
LXI B, 4220H
DAD B; HL = HL+BC = 7320+4220 = B540

## Slide 37
11. DAA (Decimal adjustment accumulator)
Used only after addition.
1 byte instruction.
The content of accumulator is changed from binary to two 4-bit BCD digits.
E.g.
MVI A, 78H ; A=78
MVI B, 42H ; B=42
ADD B ; A=A+B
DAA ; A=20, CY=1

## Slide 38
The arithmetic operation add and subtract are performed in relation to the contents of accumulator.
The features of these instructions are
1) They assume implicitly that the accumulator is one of the operands.
2) They modify all the flags according to the data conditions of the result.
3) They place the result in the accumulator.
4) They do not affect the contents of operand register or memory.
But the INR and DCR operations can be performed in any register or memory. These instructions
1) Affect the contents of specified register or memory.
2) Affect the flag except carry flag.

## Slide 39
Logical Group Instructions:
A microprocessor is basically a programmable logic chip. It can perform all the logic functions of the hardwired logic through its instruction set.
The 8085 instruction set includes such logic functions as AND, OR, XOR and NOT (Complement):
The following features hold true for all logic instructions:
1) The instructions implicitly assume that the accumulator is one of the operands.
2) All instructions reset (clear) carry flag except for complement where flag remain unchanged.
3) They modify Z, P & S flags according to the data conditions of the result.
4) Place the result in the accumulator.
5) They do not affect the contents of the operand register.

## Slide 40
The logical operations have the following instructions.
1. ANA R/M
Logically AND the contents of register/memory with the contents of accumulator.
1 byte instruction.
CY flag is reset and AC is set.
2. ANI 8 bit data
Logically AND 8 bit immediate data with the contents of accumulator.
2 byte instruction.
CY flag is reset and AC is set. Others as per result

## Slide 41
3. ORA R/M
Logically OR the contents of register/memory with the contents of accumulator.
1 byte instruction.
CY and AC is reset and other as per result.
4. ORI 8 bit data
Logically OR 8 bit immediate data with the contents of the accumulator.
2 byte instruction.
CY and AC is reset and other as per result.
5. XRA R/M
Logically exclusive OR the contents of register memory with the contents of accumulator.
1 byte instruction.
CY and AC is reset and other as per result.

## Slide 42
6. XRI 8 bit data
Logically Exclusive OR 8 bit data immediate with the content of accumulator.
2 byte instruction.
CY and AC is reset and other as per result.
7. CMA (Complement accumulator)
1 byte instruction.
Complements the contents of the accumulator.
No flags are affected.

## Slide 43
8. Logically Compare instructions
CMP R/M (1 byte instruction)
CPI 8 bit data ( 2 byte instruction)
Compare the contents of register/ memory and 8 bit data with the contents of accumulator.
Status is shown by flags & all flags are modified.
Case CY Z
[A]<[R/M] or 8 bit 1 0 A-R<0
[A]=[R/M] or 8 bit 0 1 A-R=0
[A]>[R/M] or 8 bit 0 0 A-R>0

## Slide 44
9. Logical Rotate instructions
This group has four instructions, two are for rotating left and two are for rotating right. The instructions are:
a. RLC: Rotate accumulator left
Each bit is shifted to the adjacent left position. Bit D7 becomes D0.
The carry flag is modified according to D7.
CY= D7, D7= D6, D6=D5,……,D1=D0, D0=D7

## Slide 45
b. RAL: Rotate accumulator left through carry
Each bit is shifted to the adjacent left position. Bit D7 becomes the carry bit and the carry bit is shifted into D0.
The carry flag is modified according to D7.
CY= D7, D7= D6, D6=D5,……,D1=D0, D0=CY

## Slide 46
c. RRC: rotate accumulator right
Each bit is shifted right to the adjacent position. Bit D0 becomes D7.
The carry flag is modified according to D0.
CY= D0, D7= D0,……,D0=D1

## Slide 47
d. RAR: Rotate accumulator right through carry
Each bit is shifted right to the adjacent position. Bit D0 becomes the carry bit and the carry bit is shifted into D7.
CY= D0 , D0= D1, ……..D7 = CY
Others:
10. CMC – Complement carry
11.STC- set carry flag
12. CMA – Complement Accumulator No flags effected

## Slide 48
The rotate instructions are primarily used in arithmetic multiply and divide operations and for serial data transfer.
For e.g. If A=0000 1000 = 08H
– By rotating 08H right: A=0000 0100=04.
– This is equivalent to division by 2.
– By rotating 08H left: A= 0001 0000 =10H
– This is equivalent to multiplication by 2 (10H = 1610)

## Slide 49
Branching Group Instructions:
The microprocessor is a sequential machine; it executes machine codes from one memory location to the next.
The branching instructions instruct the microprocessor to go to a different memory location and the microprocessor continues executing machine codes from that new location.
The branching instructions are the most powerful instructions because they allow the microprocessor to change the sequence of a program, either unconditionally or under certain test conditions.
The branching instruction code categorized in following three groups:
Jump instructions
Call and return instruction
Restart instruction

## Slide 50
a. Jump Instructions:
The jump instructions specify the memory location explicitly.
They are 3 byte instructions, one byte for the operation code followed by a 16 bit (2 byte) memory address.
Jump instructions can be categorized into unconditional and conditional jump.

## Slide 51
i. Unconditional Jump
8085 includes unconditional jump instruction to enable the programmer to set up continuous loops without depending only type of conditions.
E.g. JMP 16 bit address: loads the program counter by 16 bit address and jumps to specified memory location.
E.g. JMP 4000H
Here, 40H is higher order address and 00H is lower order address. The lower order byte enters first and then higher order.
The jump location can also be specified using a label or name.
E.g. MVI A, 80H START: IN 00H
OUT 43H OUT 01H
MVI A, 00H JMP START
L1: OUT 40H
INR A
JMP L1
HLT

## Slide 52
ii. Conditional Jump
The conditional jump instructions allow the microprocessor to make decisions based on certain conditions indicated by the flags.
After logic and arithmetic operations, flags are set or reset to reflect the condition of data.
These instructions check the flag conditions and make decisions to change or not to change the sequence of program.
The four flags namely carry, zero, sign and parity used by the jump instruction.

## Slide 53
Mnemonics Description
JC 16 bit Jump on carry (if CY=1)
JNC 16 bit Jump on if no carry (if CY=0)
JZ 16bit Jump on zero (if Z=1)
JNZ 16bit jump on if no zero (if Z=0)
JP 16bit jump on positive (if S=0)
JM 16bit jump on negative (if S=1)
JPE 16bit Jump on parity even (if P=1)
JPO 16bit Jump on parity odd (if P=0)

## Slide 54
b. Call and return instructions: (Subroutine)
Call and return instructions are associated with subroutine technique.
A subroutine is a group of instructions that perform a subtask.
A subroutine is written as a separate unit apart from the main program and the microprocessor transfers the program execution sequence from main program to subroutine whenever it is called to perform a task.
After the completion of subroutine task microprocessor returns to main program.
The subroutine technique eliminates the need to write a subtask repeatedly, thus it uses memory efficiently.
Before implementing the subroutine, the stack must be defined; the stack is used to store the memory address of the instruction in the main program that follows the subroutines call.

## Slide 55
1. CALL 16 bit memory
Call subroutine unconditionally.
3 byte instruction.
Saves the contents of program counter on the stack pointer.
Loads the PC by jump address (16 bit memory) and executes the subroutine.
2. RET
Returns from the subroutine unconditionally.
1 byte instruction
Inserts the contents of stack pointer to program counter.

## Slide 56
3. CC, CNC, CZ, CNZ, CP, CM, CPE, CPO
– Call subroutine conditionally.
– Same as CALL except that it executes on the basis of flag conditions.
4. RC, RNC, RZ, RNZ, RP, RM, RPE, RPO
– Return subroutine conditionally.
– Same as RET except that if executes on the basis of flag conditions

## Slide 57
Restart Instruction: 8085 instruction set includes 8 restart instructions (RST). These are 1 byte instructions and transfer the program execution to a specific location.
Restart instruction Hex Code Call location in hex
  RST 0 C7 0000H
  RST 1 CF 0008H
  RST 2 D7 0010H
  RST 3 DF 0018H
  RST 4 E7 0020H
  RST 5 EF 0028H
  RST 6 F7 0030H
  RST 7 FF 0038H
When RST instruction is executed, the 8085 stores the contents of PC on SP and transfers the program to the restart location. Actually these restart instructions are inserted through additional hardware. These instructions are part of interrupt process.

## Slide 58: Miscellaneous Group Instructions:
STACK The stack is defined as a set of memory location in R/W memory, specified by a programmer in a main memory.
These memory locations are used to store binary information temporarily during the execution of a program.
The beginning of the stack is defined in the program by using the instruction LXI SP, 16 bit address.
Once the stack location is defined, it loads 16 bit address in the stack pointer register.
Storing of data bytes for this operation takes place at the memory location that is one less than the address
e.g. LXI SP, 2099H
Here the storing of data bytes begins at 2098H and continuous in reverse order i.e 2097H.
Therefore, the stack is initialized at the highest available memory location to prevent the program from being destroyed by the stack information.

## Slide 59
The stack instructions are:
1. PUSH Rp/PSW (Store register pair on stack)
1 byte instruction.
Copies the contents of specified register pair or program status word (accumulator and flag) on the stack.
Stack pointer is decremented and content of high order register is copied. Then it is again decremented and content of low order register is copied.
2. POP Rp/PSW (retrieve register pair from stack)
1 byte instruction.
Copies the contents of the top two memory locations of the stack into specified register pair or program status word.
A content of memory location indicated by SP is copied into low order register and SP is incremented by 1. Then the content of next memory location is copied into high order register and SP is incremented by 1.

## Slide 61
XTHL – exchanges top of stack (TOS) with HL
SPHL – move HL to SP
PCHL – move HL to PC
Some instructions related to interrupt:
DI – disable interrupt
EI – Enable interrupt
SIM – set interrupt mask
RIM – read interrupt mask