## Slide 1
Assembly Language Programming
8085 Programs

## Slide 2: Store the data byte 32H into memory location 4000H.
MVI A, 32H ;Store 32H in the accumulator
STA 4000H ;Copy accumulator contents at address 4000H
HLT ;Terminate program execution
LXI H, 4000H ;Assign H= 40 and L = 00
MVI M, 32H ;load M = [HL] = [4000] = 32H
HLT ;Terminate program execution

## Slide 3: Exchange the contents of memory locations 2000H and 4000H
LDA 2000H ;the contents of memory location 2000H into accumulator
MOV B, A ;Save the contents into B register
LDA 4000H ;Get the contents of memory location 4000Hinto accumulator
STA 2000 ;Store the contents of accumulator at address 2000H
MOV A, B ;Get the saved contents back into A Register
STA 4000H ;Store the contents of accumulator at address 4000H
HLT

## Slide 4: Add the contents of memory locations 4000H and 4001H and place the result in the memory locations 4002H and 4003H (8 bit Addition).
LXI H, 4000H HL Points 4000H
MOV A, M Get first operand
INX H HL Points 4001H
ADD M Add second operand
INX H HL Points 4002H
MOV M, A Store the lower byte of result at 4002H
MVI A, 00 Initialize higher byte result with 00H
ADC A Add carry in the high byte result
INX H HL Points 4003H
MOV M, A Store the higher byte of result at 4003H
HLT Terminate program execution

## Slide 5: Subtract the contents of memory locations 4150H from 4151H and place the result in the memory locations 4152Hand 4153H (8 bit subtraction).
MVI C, 00H Initialize the C register to store borrow
LDA 4150H load the first operand
MOV B, A
LDA 4051H load the second operand
SUB B Subtract the value
JNC LOOP jump if not carry
CMA complements the accumulator to calculate 2' complement
INR A
INR C
LOOP: STA 4152 store the difference
MOV A, C
STA 4153 store the borrow
HLT

## Slide 6
Add the 16-bit number in memory locations 4000H and 4001H to the 16-bit number in memory locations 4002H and 4003H. The most significant eight bits of the two numbers to be added are in memory locations 4001H and 4003H. Store the result in memory locations 4004H and 4005H with the most significant byte in memory location 4005H. (Without carry)

## Slide 7
LHLD 4000H Get first I6-bit number in HL
XCHG Save first I6-bit number in DE
LHLD 4002H Get second I6-bit number in HL
MOV A, E Get lower byte of the first number
ADD L Add lower byte of the second number
MOV L, A Store result in L Register
MOV A, D Get higher byte of the first number
ADC H Add higher byte of the second number with CARRY
MOV H, A Store result in H Register
SHLD 4004H Store I6-bit result in memory locations 4004H and 4005H
HLT Terminate program execution

## Slide 8
Add the 16-bit number in memory locations 4000H and 4001H to the 16-bit number in memory locations 4002H and 4003H. The most significant eight bits of the two numbers to be added are in memory locations 4001H and 4003H. Store the result in memory locations 4004H and 4005H with the most significant byte in memory location 4005H. (With carry)

## Slide 9
LHLD 4000h
XCHG
LHLD 4002h
MVI B 00H
MOV A E
ADD L
MOV L A
MOV A D
ADC H
JNC LOOP
INR B
LOOP: MOV H A
SHLD 4004h
MOV A B
STA 4006h
HLT

## Slide 10
Subtract the 16-bit number in memory locations 4002H and 4003H from the 16-bit number in memory locations 4000H and 4001H. The most significant eight bits of the two numbers are in memory locations 4001H and 4003H. Store the result in memory locations 4004H and 4005H with the most significant byte in memory location 4005H. (Big – small)

## Slide 11
LHLD 4000H Get first 16-bit number in HL
XCHG Save first 16-bit number in DE
LHLD 4002H Get second 16-bit number in HL
MOV A, E Get lower byte of the first number
SUB L Subtract lower byte of the second number
MOV L, A Store the result in L register
MOV A, D Get higher byte of the first number
SBB H Subtract higher byte of second number with borrow
MOV H, A Store l6-bit result in memory locations 4004H and 4005H.
SHLD 4004H Store l6-bit result in memory locations 4004H and 4005H.
HLT Terminate program execution

## Slide 12
Subtract the 16-bit number in memory locations 4002H and 4003H from the 16-bit number in memory locations 4000H and 4001H. The most significant eight bits of the two numbers are in memory locations 4001H and 4003H. Store the result in memory locations 4004H and 4005H with the most significant byte in memory location 4005H. (Small – big)

## Slide 13
LHLD 4000H
XCHG
LHLD, 4002H
MVI B, 00H
MOV A, E
SUB L
CMA
INR A
MOV L,A
MOV A, D
SUB H
CMA
MOV H, A
INR B
MOV A, B
STA 4006h
SHLD 4004h
HLT

## Slide 14: Write an ASP to MULTIPLY two 8 bit numbers
MVI D, OOH
MVI A, 00H
LXI H, 4150
MOV B, M
INX H
MOV C, M
LOOP: ADD B
JNC NEXT
INR D
NEXT: DCR C
JNZ LOOP
STA 4152
MOV A, D
STA 4153
HLT

## Slide 15: Write an ASP to DIVIDE two 8 bit numbers
LXI H, 4150
MOV B, M
MVI C, 00H
INX H
MOV A, M
NEXT: CMP B
JC LOOP
SUB B
INR C
JMP NEXT
LOOP: STA 4152
MOV A, C
STA 4153
HLT

## Slide 16: Write an ASP to transfer a ten block of data stored from the memory location 2050H to the new memory location starting from the address 2070H.
LXI H, 2050H
LXI D, 2070H
MVI B, OAH ; setting up the counter
NEXT: MOV A, M
STAX D
INX H
INX D
DCR B
JNZ NEXT
HLT

## Slide 17: Write an ASP to generate first 10 odd numbers
MVI A, 01H
MVI B, 02H
MVI C, 0AH
LXI H, 4200H
LOOP: ADD B
MOV M, A
INX H
DCR C
JNZ LOOP

## Slide 18: Write an ASP to generate first 10 even numbers.
MVI A, 00H
MVI B, 02H
MVI C, 0AH
LXI H, 4200H
LOOP: ADD B
MOV M, A
INX H
DCR C
JNZ LOOP

## Slide 19: Example of PUSH & POP
LXI SP, 1FFFH
LXI H, 9320H
LXI B, 4732H
LXI D, ABCDH
MVI A, 34H
PUSH H
PUSH B
PUSH D
PUSH PSW
POP H
POP B
POP D
POP PSW
HLT

## Slide 20
BEORE EXECUTION
H= 93 L= 20
B= 47 C=32
D= AB E=CD
A= 34 F= 10
AFTER EXECUTION
H= 34 L=10
B=AB C=CD
D= 47 E=32
A= 93 F=20

## Slide 21: Write an ASP to find largest number in an array.
LXI H, 4200H
MOV B, M
INX H
MOV A, M
DCR B
LOOP: INX H
CMP M
JNC SKIP
MOV A, M
SKIP: DCR B
JNZ LOOP
STA 4300
HLT

## Slide 22: Write an ASP to find smallest number in an array
LXI H, 4200H
MOV B, M
INX H
MOV A, M
DCR B
LOOP: INX H
CMP M
JC SKIP
MOV A, M
SKIP: DCR B
JNZ LOOP
STA 4300H
HLT

## Slide 23: Write an ASP to sort an array in the ascending order.
MVI C, 0AH
DCR C
REPEAT: MOV D, C
LXI H, 4201H
LOOP: MOV A, M
INX H
CMP M
JC SKIP
MOV B, M
MOV M, A
DCX H
MOV M, B
INX H
SKIP: DCR D
JNZ LOOP
DCR C
JNZ REPEAT
HLT

## Slide 24: Write an ASP to sort an array in the descending order.
MVI C,0AH
DCR C
REPEAT: MOV D, C
LXI H, 4201H
LOOP: MOV A, M
INX H
CMP M
JNC SKIP
MOV B, M
MOV M, A
DCX H
MOV M, B
INX H
SKIP: DCR B
JNZ LOOP
DCR C
JNZ REPEAT
HLT

## Slide 25: WAP to multiply two 16 bit number.
LHLD 4200H Get the 1st data in HL
SP HL Save it in stack pointer
LHLD 4202H Get the 2nd data in HL
XCHG Exchange ‘HL’ and ‘DE’
LXI H 0000H Make HL – 0000
LXI B 0000H Make BC – 0000
Next: DAD SP Add ‘SP’ and ‘HL’
JNC Loop
INX B Increment ‘BC’ by one

## Slide 26
Loop: DCX D Decrement ‘DE’ by one
MOV A,E Make E – A
ORA D ‘OR’ gate between A & D
JNZ Next Jump on if number zero
SHLD 4204H Store the LSB in memory
MOV L,C Make C to L 411D 60
MOV H,B Make B to H
SHLD 4206H Store the MSB in memory
HLT Stop the program

## Slide 27: Exercise
A table having starting address 3060h contains ten numbers of 8-bit data. Write a program in 8085 that transfer the data to next table having starting address 3070h if the data is less than 90h else store it to next table at 3080h.
Write a program in 8-bit microprocessor to store 45h, A0h, B5h and 15h in the memory location starting from 4000h. Add these data and store the result in 5000h and carry flag in 5oolh
Write a program in 8-bit Microprocessor to store 68h, B3h, COh, and 11h in the memory location starting from 3000h. Move these data and store in the memory location starting from 3200h.
Write a program in 8-bit Microprocessor to store 60h, BAh, 7Ch, and 10h in the memory location starting from 2000h. Add these data and store the result in 3000h and carry flag in 5000lh. Explain all the steps.